## Slide 1: Real-Time Systems Design
Chapter 9

## Slide 2: Lesson Objectives
Introduce some terms related to real-time system
Describe the design process for real-time system

## Slide 3: Real-Time System
Correct Functioning
Result produced
Timing

## Slide 4: Real-time System
A real-time system is a software system whose correct functioning depends on the results produced and the time at which these results are produced.
Example: air traffic control systems, process control systems, and autonomous driving systems.

## Slide 5: Real-Time System
“Soft” Real Time System
Operation degraded

## Slide 6: Real-Time System
“Hard” Real Time System
Operation is incorrect

## Slide 7: Real-time System
A "soft" real-time system is a system whose operation is degraded if results are not produced according to the specified timing requirements.
Example?
A "hard" real-time system is a system whose operation is incorrect if results are not produced according to the timing specification.
Example?

## Slide 8: Stimuli of Real Time System
Event/
Stimuli
System Change States

## Slide 9: Stimuli of Real Time System
System Change States
State Machine Modeling

## Slide 10: Stimuli of Real-time System
Real-time systems have to respond to events occurring at irregular intervals. These events (or stimuli) often cause the system to move to a different state.
Thus, may be used as a way of describing astate machine modeling real-time system.

## Slide 11: Stimuli of Real-time System
A state model of a system assumes that, at any time, the system is in one of a number of possible states.
An example of state model of a simple microwave oven, extracted from the text book.

## Slide 12: Stimuli of Real Time System
Idle
Full Power On
Half Power On
Set Time
Operation Enabled
Operation Disabled
Timed Operation
Cooking Complete
Idle
Full Power
Half Power
Full Power
Half Power
Timer
Timer
Door Opened
Door Closed
Start
Door Opened
Time out
State Machine Model of a Microwave Oven

## Slide 13: Stimuli of Real Time System
Real Time System
Stimulus/Response System

## Slide 14: Stimuli of Real Time System
1. Periodic Stimulus
Two classes of Stimulus
2. Aperiodic Stimulus

## Slide 15: Stimulus/response System
One way of looking at a real-time system is as a stimulus/response system.
Stimuli fall into two classes: -
  1) Periodic stimuli
  – These occurs at predictable time intervals. E.g. the system will examine a sensor every 50ms & take action (respond) depending on the sensor value (stimulus).

## Slide 16: Stimulus/response System
Stimuli fall into two classes: -
  2) Aperiodic stimuli
  – These occurs irregularly (usually signaled using the computer’s interrupt mechanism).
  - E.g. I/O interrupt in a comp system 🡪 indicating that an I/O transfer was complete & that data was available in a buffer.

## Slide 17: Stages of RT System Design
Stimulus
Timing Constraints
Concurrent Processes
Algorithm
Scheduling system
RT OS

## Slide 18: Stages of RT System Design
Movement Detector Process
Door Sensor Process
Window Sensor Process
Building Monitor Process
Alarm System Process
Communication Process
Voice Synthesizer Process
Lighting Control Process
Audible Alarm Process
Power Switch Process
Detector Status
Sensor Status
Power Failure Interrupt
Alarm System
Alarm System
Room No.
Room No.
Alert Message
Alarm System
Alarm System
Building Monitor
400Hz
60Hz
100Hz
Notes: Periodic process
Aperiodic process
Concurrent process

## Slide 19: Stages of RT System Design
Stimulus
Timing Constraints
Concurrent Processes
Intruder Alarm System
Stimuli
Intruder alarm
(intruder alarm is triggered)
Response
Compute room no.
Call to police
Initiate voice synthesizer
Switch on audible alarm
Switch on light
Identify the stimuli that the system must process and the associated responses

## Slide 20: Stages of RT System Design
Intruder Alarm System
timing
Stimuli 🡪 Response
Stimulus
Timing Constraints
Concurrent Processes
2. For each stimulus and associated response, identify the timing constraints which apply to both stimulus and response processing

## Slide 21: Stages of RT System Design
Intruder Alarm System
Window Sensors 🡪 Windows Sensor Process
Door Sensors 🡪 Door Sensor Process
Motion Sensors 🡪 Motion Sensor Process
Stimulus
Timing Constraints
Concurrent Processes
Concurrent processes

## Slide 22: Stages of RT System Design
Scheduling system
RT OS
Intruder Alarm System
timing
Stimuli 🡪 Response
Computation algorithm
Algorithm
4. For each stimulus and response, design algorithms to carry out the required computations

## Slide 23: Stages of RT System Design
Algorithm
RT OS
Intruder Alarm System
timing
A set of stimuli 🡪 Responses
Computation algorithm
A set of concurrent processes
+
Scheduling system
Scheduling system

## Slide 24: Stages of RT System Design
Algorithm
Scheduling system
RT OS
Intruder Alarm System
Manages processes & resources allocation such as processor & memory in RT system

## Slide 25: Stages of RT System Design
Stimulus
Timing Constraints
Concurrent Processes
Algorithm
Scheduling system
RT OS
Intruder Alarm System

## Slide 26: Stages of RT System Design
Identify the stimuli that the system must process and the associated responses
For each stimulus and associated response, identify the timing constraints which apply to both stimulus and response processing
Aggregate the stimulus and response processing into a number of concurrent processes.
For each stimulus and response, design algorithm to carry out the required computations
Design a scheduling system which will ensure that processes are started in time to meet their deadlines
Integrate the system under the control of a real-time operating system

## Slide 27: Real Time System Design
Real time system must respond to stimulus at different time. Its architecture must therefore be organized so the control is transferred to the appropriate handler for that stimulus as soon as it is received.
Which control model is suitable for real-time system?

## Slide 28: Real Time Operating System
Allocate Memory & Resources
Stop Processes
Stimulus
RTOS
Manages processes and resource allocation

## Slide 29: Real-time Operating System (RTOS)
A RTOS is analogous to an operating system in a general-purpose computer.
It manages processes and resource allocation in a real-time system.
Eg: It starts and stops appropriate processes so that stimuli can be handled, and allocates memory and processor resources.

## Slide 30: Real Time Operating System
RTOS
RT Clock
Interrupt Handler
Scheduler
Resource Manager
Dispatcher

## Slide 31: Components of RTOS
Real-time clock – provides info to schedule processes periodically
Interrupt handler – manages aperiodic request for service
Scheduler – examine the processes which can be executed & choosing one of these for execution
Resource manager
Dispatcher
Diagram of RTOS

## Slide 32: Real Time Operating System
Scheduler
Interrupt handler
Real Time Clock
Resource Manager
Dispatcher
Scheduling Information
Process Resource Requirements
Available Resource List
Ready List
Processor List
Executing Process
Processes Awaiting Resources
Ready Processes
Released Processes

## Slide 33: Priority Level of Stimulus
Clock Level
Interrupt Level

## Slide 34: Priority Level of Stimulus
Interrupt level – highest priority level. It is allocated to processes which need a very fast response.
Clock level – allocated to periodic processes.

## Slide 35: Monitoring & Control Systems
Periodically poll a set of sensors
Issue command to actuator

## Slide 36: Monitoring and control systems
Monitoring and control systems are periodically poll a set of sensors, which capture information from the system's environment. They take actions, depending on the sensor readings, by issuing command to actuators.
Let’s discuss the an example of this system Intruder alarm system (diagram) from the textbook

## Slide 37: Monitoring & Control Systems
Movement Detector Process
Door Sensor Process
Window Sensor Process
Building Monitor Process
Alarm System Process
Communication Process
Voice Synthesizer Process
Lighting Control Process
Audible Alarm Process
Power Switch Process
Detector Status
Sensor Status
Power Failure Interrupt
Alarm System
Alarm System
Room No.
Room No.
Alert Message
Alarm System
Alarm System
Building Monitor

## Slide 38: Monitoring & Control Systems
Real-time system design process with example
There are several stages in the design process for real-time embedded software (alarm system with door sensors, window sensors and motion detector)

## Slide 39: Monitoring & Control Systems
Real-time system design process with example
Identify the stimuli that the system must process and the associated responses
Stimuli 🡪 Response
Example:
Stimuli (Intruder Alarm) 🡪 Response (computer room no., call to police, initiate voice synthesizer, switch on audible alarm, switch on light)
Stimuli (power failure) 🡪 Response (switch to backup power)

## Slide 40: Monitoring & Control Systems
Real-time system design process with example
For each stimulus and associated response, identify the timing constraints which apply to both stimulus and response processing
Stimuli 🡪 Response
timing

## Slide 41: Monitoring & Control Systems
Real-time system design process with example
Stimulus/response | Timing requirement
Power fail interrupt | The switch to backup power must be complete within a deadline of 50 ms
Door alarm | Each door alarm should be polled twice per second
Window alarm | Each window alarm should be polled twice per second
Motion sensor | Each motion sensor should be polled once per second
Audible alarm | The audible alarm should be switched on within 0.5 second
Lights switch | The lights should be switched on within 0.5 second of an alarm being raised by sensor
Communications | The call to the police should be started within 2 seconds of an alarm being raised by a sensor
Voice synthesizer | A synthesized message should be available within 4 seconds of an alarm being raised by a sensor

## Slide 42: Monitoring & Control Systems
Real-time system design process with example
Aggregate the stimulus and response processing into a number of concurrent processes
A set of Stimuli 🡪 Response A set of concurrent processes
timing
Example:
Window Sensors 🡪 Window Sensors Process
Door Sensors 🡪 Door Sensors Process
Motion Sensors 🡪 Motion Sensors Process
Notes: roc

## Slide 43: Monitoring & Control Systems
Real-time system design process with example
For each stimulus and response, design algorithms to carry out the required computations
A set of Stimuli 🡪 Response
timing
Computation Algorithm
Notes: roc

## Slide 44: Monitoring & Control Systems
Real-time system design process with example
Design a scheduling system which will ensure that processes are started in time to meet their deadlines
A set of Stimuli 🡪 Response
timing
Computation Algorithm
A set of concurrent processes
Scheduling System
+
Notes: roc

## Slide 45: Monitoring & Control Systems
Real-time system design process with example
Design a scheduling system which will ensure that processes are started in time to meet their deadlines
Time (second) | Action
Every 0.5 sc | Poll door sensor Poll window sensor
Every 1 sc | Poll motion sensor
Notes: roc

## Slide 46: Monitoring & Control Systems
Real-time system design process with example
Integrate the system under the control of a real-time operating system (manages processes and resources allocation such as processor & memory in real-time system)
Notes: roc

## Slide 47: Quiz
Identify ONE stimuli and corresponding/ associated responses for a carpark system.
A carpark system consists of the following hardware:
  Sensor
  Barrier
  Ticket machine
  Stimuli (… …) 🡪 Response (… …)